Lunar Entry and Approach
Platform for Research on Ground
(LEAPFROG)
GENERATION - 2
SPACE ENGINEERING RESEARCH CENTER
Fall 2019 – Spring 2021
Members
Prof. David Barnhart	barnhart@isi.edu	PI
Antariksh Narain	antariks@usc.edu	Student Researcher
Michael Smat	msmat@usc.edu	Student Researcher
Isabel Yarwood Perez	yarwoodp@usc.edu	Student Researcher

Table 1: Members List

TODOs:
Update Bibliographical database entry and mapping

# Preface
## Project Description
Moon(Lunar) exploration has been generating great interest, as it provides a compelling opportunity to demonstrate new technologies that could help build self-sustaining outposts in extraterrestrial environments, particularly Mars. The key to lasting success in this challenge lies in developing sustainable and reusable architectures. Many of the diverse global lunar missions currently in development have narrowly defined purposes. These projects are and are capable of operating in limited areas on the lunar surface and while executing specific predetermined tasks. The mass sent up for the mission therefore rarely serves more than a single purpose. The project Lunar Entry and Approach Platform for Research on Ground (LEAPFROG-Gen2), aims with the primary goal of to rethink the function of reinventing a lunar lander such that it has the inherent capability to perform multiple tasks by changing the working configuration of its subsystems, maximizing the functional value of its mass. LEAPFROG is a low-cost testbed primarily for simulating lunar flight conditions on Earth.
## Milestones
The vehicle should,
- Flight time of 5 minutes
- Max. altitude 5 meters
- Self landing in case of emergency
- Real-time telemetry to ground station
- Control over altitude +/- 0.5 meters
- Control over tilt +/- 0.5 degree
Optional
Flight to simulation experience
The project should,
- Analyze system in detail
- Plots related to performance analysis
## Timelines
Please refer the Project Libre file,
- Fall 2020 Leapfrog_Plan_Fall_2020.pod
- Spring 2021 Leapfrog_Plan_Spring_2021.pod
## People Involved
Summer 2020
USC	UCB	UCSD
Prof. David A. Barnhart (PI) / Antariksh Narain / Micheal Smat

Fall 2020
USC	UCB	UCSD

- Spring 2021
USC	UCB	UCSD

## Credits
- Information Sciences Institute (ISI)
- California Space Consortium
## Personal Deliverable
This document describes my work and research done between Fall 2019 – Spring 2021 as part of Space Engineering Research Center (SERC).
My roles and responsibilities,
- Software Developer
- Electrical/Electronics Engineer
- Embedded Engineer
- Systems Engineer
- Team Lead
The following are the items I will be sharing (SERC Wiki | GitHub | Personal Blog)
1. Detailed project document (this).
2. Software for testing individual components with related readme files.
3. Software for ground station and flight software with detailed software design document (this).
4. Circuit diagram for testing individual components.
5. Circuit diagram for vehicle and ground station.
6. Referred documentation and links.
7. Research paper written.

# Introduction
## Overview
The project is broken down into 5 sub divisions and this document aims to define each one of them in detail and how they connect.
### Vehicle Specification
#### Flight Information
#### System Limitations
### Software Used
- Visual Studio Code – software development IDE
- Gazebo – 3D simulation environment by OSRF
- GitHub – Host code for flight software and simulation
- Confluence – Store all the updates related to the project and documentations
## Structure
The structure is being built using light weight materials with high tensile strength.
- Legs: CNT
- Shelves:
- Connectors
- Gimbal
### CAD
Dassualt’s Solids Work software is being used to design the vehicle model. The software also analyzes how the parts of the vehicle act under different kinds of stress and strain.
### Vehicle Chassis
// About vehicle chassis
### Vehicle Assembly
The vehicle is being assembled in several parts. Some parts are being 3D printed and others are being manufactured from raw material at SERC.
### Test Stand
Apart from the vehicle we are building test stands for different vehicle components and the whole vehicle itself. The goal of designing the stands is to validate hardware and software integration and performance, before actually being mounted on the vehicle.
## Electronics
To achieve the flight time and performance mentioned above, the system needs to alive and responsive all the time. The system should be able to run without any issues, and fail safe procedures should activate and execute in case of emergency. The whole control system is divided into 2 sub-systems namely,
1. Altitude Control System (ACS)
2. Thrust Vectoring Control (TVC)
### Batteries
Power analysis will be done to identify the C and power rating of batteries which will be mounted on the vehicle. The battery will be powering the actuators, sensors, control board and communication modules on the vehicle.
### Control Boards
As the system is divided into 2 sub-systems, we have divided the control logic in to modules.
- Master Controller (Raspberry Pi 4)
  - Communication to ground station
  - Share system telemetry data
  - Control the ACS.
  - Master controller for engine
- Flight Controller (PixHawk)
  - Control the Gimbal
  - Control the Engine
### Sensors
We need sensors on board which can provide information about vehicle’s position, orientation, velocity and acceleration. Also, the sensors should be able to monitor the resources on board like fuel and power status. The following sensors are being used,
- Inertial Measurement Unit (IMU)
  - Relative position, orientation, velocity and acceleration
- Global Positioning System (GPS)
- Altitude sensor
- ACS tanks pressure sensor
- Fuel tank sensor
- Battery meter
### Actuators
The whole flight system is controlled by three actuation mechanism,
Cold Gas thrusters
  - There are solenoid valves placed on the vehicle, which release cold gas at high pressure (4000psi)
  - They are used to control the principle axis of the vehicle as a whole.
Gimbal System (Roll / Pitch)
  - Linear motion is converted to rotational motion by design to move the gimbal.
  - Linear actuator with forward/backward feedback are used to achieve this.
Jet Engine
  - The engine should be able to lift the vehicle to desired altitude and should also be capable of providing force vector for translation.
#### Engine
For this generation we plan to use JetCat P300 [JCP300] engine which can generate up to 300N of thrust. The engine houses an on board Engine Control Unit (ECU) which provides an interface to communicate with the engine and also provides telemetry data.
### Communication
The communication network is divided into 2 sets,
- Controller Area Network (CAN)
  - The controllers communicate using UART
  - The sensors are connected using UART, I2C and Analog input.
- Wide Area Network(WAN)
  - To provide communication between ground station and vehicle we need a communication channel which supports multiple communication channels and provides acceptable range
    - Radio Frequency (RF) – RFD900x : Long range, short bandwidth.
    - Wifi 2.4GHz : Medium range, fair bandwidth.
## Software
The software developed is responsible for providing a controlled stable flight both in real world and simulation.
The project software can be broken down based on the deployed location,
1. Ground Station: application to control and communicate with the vehicle
2. Vehicle: flight software to manage avionics.
3. Simulation: visualize the vehicle control algorithms in virtual environment.
### Ground Station
The ground station software is responsible for
1. Test individual components on the vehicle
2. Start vehicle
3. Stop vehicle
4. Visualize vehicle position
5. View Telemetry data
### Flight Software
The flight software is designed with scalability in mind, by using object oriented paradigm. It provides interface libraries to,
1. Get feedback from sensors, additional layer to filter sensor data.
2. Move the vehicle in the environment using actuators.
3. Closed loop control logic to act in the environment.
### Simulation
The simulation environment uses the vehicle designed in CAD, which is an exact replica of actual vehicle. The world is designed to mimic the world environment on moon. The simulation uses Gazebo as a simulation environment with a combination of PX4 firmware and plugins to control the vehicle. It can be used to develop and test flight software before actually deploying on the vehicle. Actual hardware constrains can be added to the model like reaction time, sensor noise etc. to make it more realistic. Also, the simulation can be piped with actual hardware to visualize real-time movement and response.
### Validation (Testing)
The testing is divided into several stages,
1. Unit Testing the code: Validate if the code works properly and doesn’t throw any unexpected exception.
2. Communication test: how different major system communicate
3. Testing in simulation: is the flight software working
4. Testing on hardware test bench: check response based on pseudo input and check for jitters
5. Pseudo failure test: validate how system responds when each system fails
6. Actual vehicle test: test end to end flight
## Competition
### Challenges
There are 3 challenges proposed for now,
1. Waypoint Navigation(Simulation)
2. ---(Simulation)
3. Waypoint Navigation + Relative positioning (Hardware: PixHawk)
### Website
### Environment
We will setup GitHub classrooms for all the teams. It will allow teams to register with a unique name and create a private repository which can be viewed by the admin. Teams will be given clear instructions which section of the code they can edit.
The code can be compiled locally and when submitted, will be validated by an automated tester which will check if the code compiles and passes basic test (check terminal output with expected data).
### Evaluation
The teams will be evaluated based on their performance in the first 2 competitions and accordingly will be moved to challenge 3.
// Describe a little more
## Safety and Test Procedures
### Safety Standards
// Define the safety standards in place at lab and during testing of hardware.
### Test Procedures
Refer Testing section for details.

# System Overview
## Avionics Requirements
### Hardware
- Sensor calibration and library
  - Stabilization: IMU
  - Attitude control: LiDAR
  - Fuel : feedback from engine to estimate fuel consumption
  - Cold gas pressure : Pressure sensor
- Controllers
  - Main Controller: Control all actuators in the system
    - ACS system: Control solenoid valves with relays
    - TVC system: validate and translate information coming from Flight Controller.
    - Communication: communicate with the ground station.
  - Flight Controller: Computation for TVC system
- Actuators
  - Linear Actuators: Move the gimbal the engine
  - Solenoid Valves : To control cold gas release
- Communication
  - Transceiver: Radio Frequency
  - Range: radial 10m
- Engine
  - Jet Engine: To control altitude of the vehicle
  - Jet Engine interface: interface to communicate with the engine.
- Power to control all electronics on-board.
### Software
- Ground station
  - Sequentially start the system
  - Manual override custom operation
- Flight Information
  - Fuel, battery, cold gas pressure
  - Waypoint information
  - GPS position
  - Position, velocity and acceleration information
- Mission Mode
  - flight profile insertion: Send sequence of waypoints
  - autonomous flight
  - mission modes
## Performance Specification
### Software Development
#### Software
Standard Installation
1. Linux Distro: (Mint / Ubuntu)
2. Visual Studio Code
3. Draw.io
4. Libre Office
Custom Installation // Appendix reference
1. Gazebo 11
2. ROS2
3. Python Packages
4. Boost C++
#### Hardware
1. 8 GB RAM
2. 50 GB HDD/SSD.
### Electronics
Sensor	MPU6050	Accel: ±2g | Gyro: ±500°C | Onboard DMP | 400kHz I2C
	SEN0259	Range: 0.3-12m | Accuracy: ±4cm | Frequency: 100Hz
	PX309-5KG5V	Range: 0-5000psi | Analog voltage output
	HERE 3	NAVSTAR | Accuracy: 3D FIX: 2.5 m / RTK: 0.025 m | Rate: 8Hz
Controller	Raspberry Pi	Quad Core @1.5GHz | 4GB RAM | 5V | 4A
	PixCube	32bit Cortex-M4F | 256KB RAM | 14PWM pins
Battery	LiPo 11.1V	1800mAh | 45C | XT60 | 11.1V/3S
	LiPo 22.2V	2600mAh | 45C | XT60 | 22.2V/6S
Communication	RFD900x	902-928MHz | 250kbps | 5V | (max)800mA | 1Watt (+30dBm)
	Ground station	RFD900x
Actuator	HDLS-4-2-12V	Stroke length: 2” | Speed(Max load): 0.6”/sec | 12V | 1A
	Solenoid Valve (Num)
Engine	JetCat P300Pro	Max Thrust: 300N | Max power(start up): 300W | Comm: UART,PWM Integrated ECU | Engine Telemetry feedback
Others	Dbus Interface	Breakout board for DB15 connector
	Relay Board	8 channel | 5V | 100mA
	UBEC	Input: 7.2-21.V | Output: 5V, 5A

Table 2: Performance Specification - Electronics
## Software UML diagram
### Timing function
### Command Telemetry
# Architecture
## System

Figure 1: System Architecture
## Vehicle

Figure 2: Vehicle Overview
## Ground Station
## Simulation
## Competition
# Implementation – Structure

# Implementation – Electronics
## Introduction
Raspberry PI
The SoC can be powered using an adapter (5V/4A) or by powering the pins using a controlled power source like UBEC and connect the PIN4 to 5V and PIN6 to Ground.
Refer Raspberry Pi Setup for detailed instructions to configure the micro-processor.

## Modules Validation
## Avionics
# Implementation – Software
## Introduction
### Overview of the system

Figure 3: Overview of Software Architecture

### Communication flow

Figure 4: Communication Flow

### Design
As we can see in figure the system is divided into the following major component,
Ground Station
  - Send and log commands to the vehicle.
  - Get vehicle hardware data both raw and processed and show it to the user in realtime and log it.
- Flight Software
  - Initialize the system.
  - Act based on the command send by the user.
  - Log all the sensor data and command information.
  - Provide flight safety with predefined fail-safe operations.
  - Read data from other flight controller.
- Flight Controller
  - Based on the sensor data calculate the engine thrust and gimbal angle.
As similar hardware (sensor / actuator) is defined and controlled at both ends, these are defined as common property classes to maintain consistency. Also, as it makes it generic operation, the encoding and decoding command code can be reused on both ends. The additional thing that needs to be done on the ground station software is to parse user input and convert it to usable command. A change code is generated based on the logic defined below to inform what values have changed since the last update.
## Ground Station
### UML Diagram
#### Terminal Control
Manual Control
Flight Control: / Initialize System / Send Waypoints / Hover / Initialize Landing / Abort Commands / Shutdown System	Receive Commands: / Sensor Data / Position Data / Resource Data / Actuator Information	Encoding Rule: / Hex-Code: / Bit 3: MC / FC Bit 2-0: Operation type. / Value Class: / Empty→ send data / Values → update data

Flight Software
Safety Parameters: / Geo Fencing (Position) / Velocity / Heart Beat / Delay / Communication loss	Altitude / Resource Status: Cap 25% / ACS / Fuel / Battery	Control System: / ACS → Parallel Actuation (3) programs / TVC → Px4 Controller

Flow logic
1. The user is prompted to enter command on the terminal.
2. Command is stripped to identify the object and information.
3. Object points to the function to call and information is used to update class properties.
4. These properties are serialized and send via the channel.
5. The receiver deserializes the information and pass it to the mapped function which takes the appropriate action.
## Hardware Virtualization
Goal: To validate the flight safety software before deploying it on an actual hardware.
Design: The flight safety logic resides on the main controller. Sensors and actuators connect to the device using interfaces like UART, I2C, CAN, digital pins and analog pins.
- The system can test using auto-generated log files which test the logic.
- We can manually control the positioning system.
- The system can be visualized using 2 sets of plots,
  - X-Y coordinate plane
  - Z (altitude plotting)
### Modules
#### Protocols
1. UART (Laser Sensor)
   socat
   Create a virtual UART port to send and receive data.
2. I2C (IMU Sensor)
   Create a virtual I2C communication hardware with address 0x68 to write data on bus.
3. CAN (GPS)
4. Analog Input
   Not Applicable.
Note: The UART protocol can be virtualized, so all the sensor data can be transmitted using the UART.
#### Sensors
1. IMU
   Generate acceleration data using sensor mean and variance. Add functionality to manually move the mean along the axis. To test the velocity measurement.
2. GPS
   A position generating program based on direction of motion to test the Geo-fence.
3. Altimeter
   A flight profile of different cases.
   - Max altitude limit.
   - Landing test.
   - Hovering.
   Should be coupled with engine?
4. Pressure Sensor
   Gradually decreasing pressure with use.
#### Actuators
1. Engine Thrust
   Increase / decrease the thrust.
   How to couple thrust to altitude?
2. Engine Fuel
   TBD
3. Gimbal Angle
   Generate gimbal angle profile for roll and pitch over n timestamps.
4. Gimbal Linear Position
   Similar to (4)
#### Others
1. Missing Heartbeat
  Do not send packets on channel, to mimic heartbeat loss.
2. Command burst
   Some scenario where we can test the priority of command calls.

## Ground Station

## Flight Software
### Sensor Interfacing
### Safety Logic

# Implementation – Simulation
# Testing
## ACS Test
## Gimbal Test
### Electronic
Components needed for gimbal test
1. Controller: Raspberry Pi connected over WiFi.
2. IMU Sensor mounted on the innermost ring of the gimbal.
3. Relay board to power up the actuators.
4. Linear actuators (2) to move the gimbal. (Refer structure for mounting instructions)
Connection Diagram
Code Reference
Actual Setup
## Engine Static Hot Fire Test
// Test profiles to be used and tested.
## Wireless Testing
### Short Range
### Long Range
# System Analysis
## Structures
// stress strain info, graphs etc.
## Electronics
// datasheet info and data plots
## Software
// Function analysis and execution times
## Simulation
//
# How to use
## Vehicle
// Procedures to run the vehicle
## Simulation
// Setup the environment and running/ testing the code

# Safety Procedures

# Test Procedures
// Each section talks about how each procedure works

# Appendix
## Software
### Simulation
#### Gazebo
#### ROS2
### Development Environment
#### Python Packages
#### Boost C++
## Electronics
### Raspberry PI
#### Install OS
#### Enable GPIO Pins
#### Install additional packages