## Slide 1: Avionics, GNC and SW Systems Review for LEAPFROG GEN II
Requirements:
  LEAPFROG GEN II Flight Requirements
  Avionics Requirements
  GNC Requirements
  Software Requirements
System Overview and Architecture Definition
  Top Level Performance Specs
  Avionics
  Power system
  GNC Specifics
System Details
  Avionics Details
  GNC Details
  Software Details
Competition Simulation and Flight Operation Definitions
Notes: Add abort codes or mission variables, test scenarios..
1

## Slide 2: Primary Flight Requirements for LEAPFROG
Flight Goals:
  >2.5 meters in height
  10 second to 60 second max flight duration
  Stability in roll, pitch, and yaw during hover and translation (+/- 0.5 deg)
  Control over altitude (+/- 0.5 meter)
  Active abort contingencies
Off-Board Goals:
  Ground control authority
  Command override authority during flight from Ground
  Turnaround of LEAPFROG flight to flight within 15 minutes
  Analysis of accuracy and efficiency of system components
Notes: Add abort codes or mission variables, test scenarios..
2

## Slide 3: Gen II Avionics Requirements
Hardware Requirements
  Sensors for Stabilization, attitude control, and navigation
  Processor for multiple GNC algorithm systems
  Telemetry system for downlink of real time flight data, and uplink “heartbeat” for safety override
  Engine Controller for Jet Engine
  Relay Controller for ACS Thrusters
  Sufficient Power system for all primary and secondary devices, with sufficient margin for Flight
Software requirements
  Ground Operations Mode for startup, checkout, and override
  Mission Mode (flight profile insertion, autonomous flight, safety overrides)
  Flight Information (health and safety and status of all systems)

## Slide 4: GNC Requirements
Establish two methods to support Stabilization and Translation for LEAPFROG
  Primary Stabilization through Cold Gas Thrusters as Attitude Control
  Primary Translation using Thrust Vector Control (TVC) with a gimbaled Jet Engine
Each operates independent of the other, but each can provide for some level of stability in emergencies
For the Simulation and Flight Challenge, competitors will only program inputs to the TVC and Engine system
  The ACS system is independent and meant to be failsafe

## Slide 5: Software Requirements
TBD

## Slide 6: System Architecture
Full Systems Functional Layout
Power System Functional Layout
GNC System functional Layout
Etc
Must combine the following charts into something that is consistent with each other, and makes it easy to trace from hardware, to function etc.

## Slide 7: System Block Diagram

## Slide 8
Payload Antenna
Ground Computer
(Thinkpad)
Camera Interface
Ground Power
H&S Antenna
Ground
Lander
LiIon Charger
Power
C&DH
586D Controller
Comm
Payload Antenna
H&S Antenna
Wireless
Ground Jet
Controller
Fuel Shutoff
Propane Shut off
Jet Engine
12V
Jet Pump
ECU
Jet Prop.
D/A Board
4 Gimbal Motors
Camera
Cam Antenna
P/L
P/L
ACS
GNC
12 PLC or Relays
Solenoids
3 MEMS Gyros
3 MEMS Accels
Altimeter
Power Distribution Unit
5V
3.3V
9V
12V
22V
5V
Kristina Rojdev
Dec 03, 2007

## Slide 9: Software Architecture
TBD

## Slide 10: Configuration Comparison

## Slide 11: Configuration Comparison
Link to full document: https://docs.google.com/document/d/1CP5_ekTFtuK3u4mSZqckigZ51Cf-EMv6XL89iKFO6wk/edit

## Slide 12
Feedback Sensors
Gimbal
ODRIOD
Pixhawk Cube
Pos/Att Estimator
Navigator
Position Controller
Mixer
PX4
ACS Controller
ECU
Jet Engine
Pitch
Roll
Yaw
Solenoid
Demodulator
TVC
ACS
System Overview

## Slide 13
Feedback Sensors
Gimbal
Pixhawk Cube
Pos/Att Estimator
Navigator
Position Controller
Mixer
PX4
ECU
Jet Engine
Ground Control Station
QGroundControl
People/Path Planning Software
Legend For Arrows:
Waypoints/constraints/parameters
Sensor/position feedback
Position setpoints
Attitude and thrust setpoints
Thrust setpoint
Commands for actuators
TVC

## Slide 14: Links:
Documentation for uploading the firmware onto the vehicle: https://docs.px4.io/master/en/config/firmware.html
PX4 Controller Diagrams: https://dev.px4.io/master/en/flight_stack/controller_diagrams.html
Estimation/Localization library documentation: https://docs.px4.io/master/en/advanced_config/tuning_the_ecl_ekf.html

## Slide 15
PX4
Feedback Sensors
ODRIOD
ACS Controller
Pitch
Roll
Yaw
Solenoid
Demodulator
Legend For Arrows:
Sensor feedback
Duty cycle for pitch and roll cold gas thrusters/relays/solenoids
PWM corresponding to the yaw force desired
Duty cycle for yaw cold gas thrusters/relays/solenoids
Pixhawk
ACS

## Slide 16
ACS Controller
Standard PID Controller With Low-Pass Filter on D Term
Force to Duty Cycle Conversion Estimator
Attitude Feedback
Duty Cycle
ACS

## Slide 17
24V
6V
Relays
12 solenoids
Avionics Computer
Opto-isolator
D/A
Power Amp
Gimbal Motors
LDO regulator
IMU
Jet Engine
Altimeter
7.2V
Camera
Red lines are power lines and black lines are signal lines. Ground and voltage lines have not been specified.
Power System layout

## Slide 18: Detailed Systems Definitions
Avionics & Wireless System
GNC & Engine
Power
Note what follows are examples of the kind of information that should be included in various sections

## Slide 19: Top Level Performance Specs (can be actual hdwe specs or not)

## Slide 20: Common Flight Axes definitions for Code and hdwe orientation

## Slide 21: Layout of Hardware (either actual photo or CAD, doesn’t matter

## Slide 22: Define CG/MOI/CE Location/Effectos etc

## Slide 23: Avionics and Wireless Systems
Identify all the key components

## Slide 24: Avionics Primary function list (can be pseudo commands, but list of what you need the avionics to do)

## Slide 25: Avionics Timing of functions…

## Slide 26: Wireless System Requirements

## Slide 27: Command and Telemetry List
What does the wireless link have to send up and down to the vehicle

## Slide 28: Ground Control for Communications
What does it have to do?

## Slide 29: Wireless components
Show transmitter and antenna, validates it will work on larger range

## Slide 30: IMU Characteristics
Must show drift, static/dynamic displacement with accel etc

## Slide 31: GNC and Engine Control
Here need to show difference between control algorithm for ACS and TVC (example shown)

## Slide 32: ACS Schematic

## Slide 33: ACS Stability control based on vehicle characteristics
tbd

## Slide 34: ACS Valve Response
Must validate valve response is fast enough and define it, as that sets up the vehicle characteristic equation in state space to show stability (ie not bang bang)

## Slide 35: ACS Nozzle Sizing info
tbd

## Slide 36: ACS Thrust Measurement setup
This is old one, you have one in the lab, show that, and show results.

## Slide 37: ACS Air Bearing Test Objectives to validate its function
tbd

## Slide 38: TVC Schematic
Show simple diagram of how the Engine and actuators etc. Same as ACS layout, but focused on gimbal system to engine

## Slide 39: Describe engine Characteristics
tbd

## Slide 40: Describe gimbal system characteristics, response from actuators etc etc.
tbd

## Slide 41: TVC Translation Motion Plans
This was old LEAP, show yours using TVC etc

## Slide 42: TVC Control and Navigation
Show lateral displacement motion plan
Show altitude control plan
Etc.

## Slide 43: ACS Schematic

## Slide 44: Software Discussion
Safety and Abort Plans
Validation Tests planned for Software functions (nominal and abort)
Ground Control Code Plan
Flight Operations Scheduler

## Slide 45: Software Details- Safety and Abort Clauses
Safety and Abort Clauses
  Three classes of Abort Commands
    Subsystem Test Terminate
      To abort an individual subsystem preflight test. The test is aborted as soon as possible (based on preservation of system).
    Mission Abort Command
      In this class, a vehicle can be either sent an Abort Command from Ground, or the GNC can decide that it needs to Abort.
      The vehicle aborts the normal profile navigation, the attitude is fixed to normal, and the engine goes to AbortRPM.
    Mission Emergency Abort
      In this mode all operations are suspended immediately, including shut down of all Thrusters and emergency shutdown of the Jet Engine.

## Slide 46: Initial Test Validation Matrix for Software and Avionics Control

## Slide 47: Software Architecture Pseudo-Code Diagram

## Slide 48: Software Architecture (cont.)
Mission Code
Initialize GNC variables
Initialize Avionics Variables
Enable Timer Interrupts
Read Sensors
Convert Sensor Values
In_Flight = GNC_Luna()
Jet_Send
ACS_Send
Check In_Flight
Disable Timer Interrupts
RETURN TO MAIN MENU

## Slide 49
Ground Command Abort Sequences
Command/Auto | Command Pressed/Reason | Effect on Engine | Effect on controller | Effect on ACS
Emergency shutdown/ | D/ | Full shut off | None | Shutoff
Engine Idle/ | C/ | Idle | none | Off
Z toggle/ | Z/ | No change | Z controller removed, no effect on GNC | Stays On
Flight Abort/ | A/ | RPM fixed to value corresponding to thrust just below weight | Z-off, GNC is on | ACS is on
/D | Angle exceeded> +/-15degree | Full shut off | None | Shutoff
/A | Altitude > 6 m | RPM fixed to value | Z-off, GNC is on | Acs is on
/D | Flight time exceeded> t secs | Full shut off | None | Shutoff

## Slide 50
Fault Probabilities and Scenarios
Scenarios | Reason | Problems | Abort Sequence
Flight above 6 meters | Manual; engine keeps firing | Escapes net boundary | Flight Abort
Flight time > t seconds | Manual; engine keeps firing | Overheating | Emergency
Roll, Pitch > +/-15 degrees | Wind; misfiring thrusters; altimeter misreading | Tips over | Emergency
Rabbit Dies | Electrical misfires; batteries die | Controls inputs; engine may still fire | Emergency
Engine Fails | Air in fuel; electrical misfire; pump malfunction; dust | Coughs; fire damage; stalls completely | Flight Abort or Emergency
Altitude Control System | Batteries die; wires disconnect | Stabilizing thrusters won't work properly | Flight Abort
Z-controller Fails | Altimeter misreading; disconnection | Begins rotating irrationally | Flight Abort
Ground Comp Malfunctions/Dies | Battery; Bluetooth malfunction | Craft is running on auto | No sequence
Power Fails Non-uniformly | Batteries die; wires disconnect | See Rabbit, Engine, Controller dies | Flight Abort or Emergency
Power Fails Uniformly | Batteries die; wires disconnect | Machine drops to ground as engine stops | Flight Abort or Emergency

## Slide 51: Abort and Mission Variables would be programmed into onboard Avionics prior to flight
Notes: 51

## Slide 52: Show a simple intrgation and build and test flow
Notes: 52

## Slide 53: Need to identify key risk areas and show we are mitigating them.
Notes: 53