## Slide 1
Avionics, GNC and SW Systems Review for LEAPFROG GEN II
Requirements:
  LEAPFROG GEN II Flight Requirements
  Competition Requirements
  Avionics Requirements
  GNC Requirements
  Software Requirements
System Overview and Architecture Definition
  CONOPS for Flight
  Top Level Performance Specs
  Avionics
  Engine system
  GNC Specifics
System Details
  Avionics Details
  GNC Details
  Software Details
Competition Simulation and Flight Operation Definitions
Notes: Add abort codes or mission variables, test scenarios..
<number>

## Slide 2
Primary Flight Requirements for LEAPFROG
Flight Goals:
  >2.5 meters in height
  10 second to 60 second max flight duration
  Stability in roll, pitch, and yaw during hover and translation (+/- 0.5 deg)
  Control over altitude (+/- 0.5 meter)
  Active abort contingencies
Off-Board Goals:
  Ground control authority
  Command override authority during flight from Ground
  Turnaround of LEAPFROG flight to flight within 15 minutes
  Analysis of accuracy and efficiency of system components
Notes: Add abort codes or mission variables, test scenarios..
<number>

## Slide 3
Artemis LEAPFROG Competition Requirements (Belzberg et al)
Goals
  Provide off-board remote capability for teams to develop flight algorithms using LEAFPROG components
  Provide them basics on vehicle dynamics, characteristics, sensor capabilities
  Tie the software pre-flight challenge, to the flight challenge
Implementation Recommendations
  Fly a separate COTS based microprocessor that can be purchased by any/all teams (PixHawk)
  Develop onboard LEAP an override function that continues nominal flight to land, if the competition team code or flight algorithms are off-nominal
  Provide competition teams specific limits on key variables:
    Altitude
    Altitude rate
    X, Y field location limits (Geo Fence)
    Velocity of vehicle
    Angle of Gimbal commanded

## Slide 4
Gen II Avionics Requirements (Antariksh)
Hardware Requirements
  Sensors calibration and library
    Stabilization: IMU (MPU6050)
    Attitude control: LiDAR (SEN0259)
    Resource status
      Fuel: estimation
      Cold gas: pressure sensor
    Navigation: PixHawk (Controller + GPS)
  Processors
    Main Controller : Raspberry Pi
    Navigation Controller : PixHawk
  Telemetry system for downlink of real time flight data, and uplink “heartbeat” for safety override
  Engine Controller for Jet Engine
  Relay Controller for ACS Thrusters
  Sufficient Power system for all primary and secondary devices, with sufficient margin for Flight
Software requirements
  Ground Operations Mode for startup, checkout, and override
  Mission Mode (flight profile insertion, autonomous flight, safety overrides)
  Flight Information (health and safety and status of all systems)

## Slide 5
GNC Requirements
Establish two methods to support Stabilization and Translation for LEAPFROG
  Primary Stabilization through Cold Gas Thrusters as Attitude Control
  Primary Translation using Thrust Vector Control (TVC) with a gimbaled Jet Engine
    Backup Stabiliization
Each operates independent of the other, but each can provide for some level of stability in emergencies
For the Simulation and Flight Challenge, competitors will only program inputs to the TVC and Engine system
  The ACS system is independent and meant to be failsafe

## Slide 6
Software Requirements
TBD

## Slide 7
System Architecture (Dave b)
CONOPS
Full Systems Functional Layout
GNC System functional Layout
ACS System functional layout
TVC System Functional Layout
S/W Flow diagram
Power System Functional Layout
Must combine the following charts into something that is consistent with each other, and makes it easy to trace from hardware, to function etc.

## Slide 8
CONOPS for Flight Competition (Daniel/Thanh et al)
RC Airplane Pits: LEAPFROG Fueling and Pre-Flight C/O
RC Field supports Audience Member Viewing Stands for public involvement
LEAPFROG Operations Center:
Up to 500 meter range
Wireless signal booster
Laptop Control
RC Airfield provides T/O and Landing Sites
Competition Field uses RC Fields
Possible Competition Metrics:
Flight Time
Stability and Hold
Navigation Precision
Fuel Useage
Multi-Hop Translation
Various Guidance Challenges
Etc
LEAPFROG Sets up PostFlight Assessment and Scoring

## Slide 9
System Block Diagram

## Slide 10
Payload Antenna
Ground Computer
(Thinkpad)
Camera Interface
Ground Power
H&S Antenna
Ground
Lander
LiIon Charger
Power
C&DH
586D Controller
Comm
Payload Antenna
H&S Antenna
Wireless
Ground Jet
Controller
Fuel Shutoff
Propane Shut off
Jet Engine
12V
Jet Pump
ECU
Jet Prop.
D/A Board
4 Gimbal Motors
Camera
Cam Antenna
P/L
P/L
ACS
GNC
12 PLC or Relays
Solenoids
3 MEMS Gyros
3 MEMS Accels
Altimeter
Power Distribution Unit
5V
3.3V
9V
12V
22V
5V
Kristina Rojdev
Dec 03, 2007

## Slide 11
Software Architecture
TBD

## Slide 12
Feedback Sensors
Gimbal
ODRIOD
Pixhawk Cube
Pos/Att Estimator
Navigator
Position Controller
Mixer
PX4
ACS Controller
ECU
Jet Engine
Pitch
Roll
Yaw
Solenoid
Demodulator
TVC
ACS
System Overview

## Slide 13
Feedback Sensors
Gimbal
Pixhawk Cube
Pos/Att Estimator
Navigator
Position Controller
Mixer
PX4
ECU
Jet Engine
Ground Control Station
QGroundControl
People/Path Planning Software
Legend For Arrows:
Waypoints/constraints/parameters
Sensor/position feedback
Position setpoints
Attitude and thrust setpoints
Thrust setpoint
Commands for actuators
TVC

## Slide 14
Links:
Documentation for uploading the firmware onto the vehicle: https://docs.px4.io/master/en/config/firmware.html
PX4 Controller Diagrams: https://dev.px4.io/master/en/flight_stack/controller_diagrams.html
Estimation/Localization library documentation: https://docs.px4.io/master/en/advanced_config/tuning_the_ecl_ekf.html

## Slide 15
PX4
Feedback Sensors
ODRIOD
ACS Controller
Pitch
Roll
Yaw
Solenoid
Demodulator
Legend For Arrows:
Sensor feedback
Duty cycle for pitch and roll cold gas thrusters/relays/solenoids
PWM corresponding to the yaw force desired
Duty cycle for yaw cold gas thrusters/relays/solenoids
Pixhawk
ACS

## Slide 16
ACS Controller
Standard PID Controller With Low-Pass Filter on D Term
Force to Duty Cycle Conversion Estimator
Attitude Feedback
Duty Cycle
ACS

## Slide 17
24V
6V
Relays
12 solenoids
Avionics Computer
Opto-isolator
D/A
Power Amp
Gimbal Motors
LDO regulator
IMU
Jet Engine
Altimeter
7.2V
Camera
Red lines are power lines and black lines are signal lines. Ground and voltage lines have not been specified.
Power System layout

## Slide 18
Detailed Systems Definitions
Avionics & Wireless System
GNC
Engine
Note what follows are examples of the kind of information that should be included in various sections

## Slide 19
Top Level Performance Specs (can be actual hdwe specs or not)
Antarkish for electronics
Michael S for vehicle structure
Kendra for ACS System
TBD for Jet Engine System

## Slide 20
Common Flight Axes definitions for Code and hdwe orientation
Andrew

## Slide 21
Layout of Hardware (either actual photo or CAD, doesn’t matter
Michael et al

## Slide 22
Define CG/MOI/CE Location/Effects etc
Michael/Andrew

## Slide 23
Avionics and Wireless Systems
Antariksh

## Slide 24
11/10/2020
<number>
Avionics uses COTS Processor(s)
Current Circuit Design
IMU
Odroid XU4
Relay Board
Grounding Blocks
Notes: How is the data from the MCU consumed by the Gimbal
<number>

## Slide 25
Avionics Primary function list (can be pseudo commands, but list of what you need the avionics to do)
Antariksh

## Slide 26
Avionics Timing of functions…
Antariksh

## Slide 27
Wireless System Requirements
Antariksh/Daniel

## Slide 28
Command and Telemetry List (Antariksh + ?)
What does the wireless link have to send up and down to the vehicle

## Slide 29
Ground Control for Communications (Antariksh)
What does it have to do?

## Slide 30
Wireless components (Antariksh)
Show transmitter and antenna, validates it will work on larger range

## Slide 31
IMU Characteristics (Jose?)
Must show drift, static/dynamic displacement with accel etc

## Slide 32
GNC and Engine Control
LEAPFROG has two methods for stability and translation
  Cold Gas Attitude Control System
  Thrust Vector Control for Engine
A comparison on best method to combine or separate functions was executed early on the program

## Slide 33
Early analysis on Engine Torque to ACS response
Link to full document: https://docs.google.com/document/d/1CP5_ekTFtuK3u4mSZqckigZ51Cf-EMv6XL89iKFO6wk/edit

## Slide 34
TVC/ACS configurations evaluated

## Slide 35
Option X Selected: But challenges exist with two different control methods and systems (Nikita)
Plan is to use each for separate functions
  Cold Gas Attitude Control System for Vehicle platform stability relative to Earth
  Thrust Vector Control of Engine for Translation
Both are operated and commanded from the primary avoicis processor (Arduino)
  For Student competition challenge, each team will program a PixHawk controller, that is independent from Arduino
  But all commands to engine and TVC actuator go through Arduino
Key challenges:
  Timing differences between what is sent from PixHawk to Arduino
  Delays induced
  Instability from TVC adds to ACS
  Instability from ACS adds to TVC
  TBD

## Slide 36
Initial Test Matrix to validate from Simulation to Hardware for all GNC (Nikita)
Identify a matrix here that shows each simulation, and then a hardware test to validate it.

## Slide 37
ACS Schematic (Kenya)

## Slide 38
ACS Stability control based on vehicle characteristics
Kenya

## Slide 39
ACS Valve Response (Kenya)
Must validate valve response is fast enough and define it, as that sets up the vehicle characteristic equation in state space to show stability (ie not bang bang)

## Slide 40
ACS Nozzle Sizing info (Kenya)
tbd

## Slide 41
ACS Thrust Measurement setup (Kenya, show from Spring 2019)
This is old one, you have one in the lab, show that, and show results.

## Slide 42
ACS Air Bearing Test Objectives to validate its function
Kenya

## Slide 43
TVC Schematic (Andrew)
Show simple diagram of how the Engine and actuators etc. Same as ACS layout, but focused on gimbal system to engine

## Slide 44
11/10/2020
<number>
3 concentric rings
Relative rotations thanks to the presence of connecting pins
Pins aligned with principal axis of inertia
Gimbal Ring Design
VERTICAL CONFIGURATION
DISPLACED CONFIGURATION
Notes: How is the data from the MCU consumed by the Gimbal
<number>

## Slide 45
11/10/2020
<number>
1st LEAPFROG TVC Gimbal mechanism

## Slide 46
11/10/2020
<number>
TVC System uses linear actuators
Horizontal position to maximize actuation speed
Reduced distance from the center of rotation to maximize angular displacement
Aligned with principal axis of inertia
18.4 deg/s
Describe gimbal system characteristics, response from actuators etc etc.
Notes: How is the data from the MCU consumed by the Gimbal
<number>

## Slide 47
11/10/2020
<number>
Gimbal angles defined
-90 < xi < 90
-5 < delta < 5
Notes: How is the data from the MCU consumed by the Gimbal
<number>

## Slide 48
11/10/2020
<number>
Gimbal System Prelim Analysis (Andrew update with yours?)
Notes: How is the data from the MCU consumed by the Gimbal
<number>

## Slide 49
Describe engine Characteristics
Engine person and Andrew?

## Slide 50
TVC Translation Motion Plans (Andrew)
This was old LEAP, show yours using TVC etc

## Slide 51
TVC Control and Navigation (Andrew)
Show lateral displacement motion plan
Show altitude control plan
Etc.

## Slide 52
TVC State Simulation Results (Andrew)

## Slide 53
Software Plans and Architecture (Antariksh)
Competition Simulation Software: (Thanh)
Competition Flight Software: (?)
Onboard LEAPFROG Software (Antariksh)
Safety and Abort Plans
Validation Tests planned for Software functions (nominal and abort)
Ground Control Code Plan
Flight Operations Scheduler

## Slide 54
Software Details- Safety and Abort Clauses
Safety and Abort Clauses
  Three classes of Abort Commands
    Subsystem Test Terminate
To abort an individual subsystem preflight test. The test is aborted as soon as possible (based on preservation of system).
    Mission Abort Command
In this class, a vehicle can be either sent an Abort Command from Ground, or the GNC can decide that it needs to Abort.
The vehicle aborts the normal profile navigation, the attitude is fixed to normal, and the engine goes to AbortRPM.
    Mission Emergency Abort
In this mode all operations are suspended immediately, including shut down of all Thrusters and emergency shutdown of the Jet Engine.

## Slide 55
Initial Test Validation Matrix for Software and Avionics Control

## Slide 56
Software Architecture Pseudo-Code Diagram

## Slide 57
Software Architecture (cont.)
Mission Code
Initialize GNC variables
Initialize Avionics Variables
Enable Timer Interrupts
Read Sensors
Convert Sensor Values
In_Flight = GNC_Luna()
Jet_Send
ACS_Send
Check In_Flight
Disable Timer Interrupts
RETURN TO MAIN MENU

## Slide 58
Ground Command Abort Sequences
Command/Auto | Command Pressed/Reason | Effect on Engine | Effect on controller | Effect on ACS
Emergency shutdown/ | D/ | Full shut off | None | Shutoff
Engine Idle/ | C/ | Idle | none | Off
Z toggle/ | Z/ | No change | Z controller removed, no effect on GNC | Stays On
Flight Abort/ | A/ | RPM fixed to value corresponding to thrust just below weight | Z-off, GNC is on | ACS is on
/D | Angle exceeded> +/-15degree | Full shut off | None | Shutoff
/A | Altitude > 6 m | RPM fixed to value | Z-off, GNC is on | Acs is on
/D | Flight time exceeded> t secs | Full shut off | None | Shutoff
Notes: <number>

## Slide 59
Fault Probabilities and Scenarios
Scenarios | Reason | Problems | Abort Sequence
Flight above 6 meters | Manual; engine keeps firing | Escapes net boundary | Flight Abort
Flight time > t seconds | Manual; engine keeps firing | Overheating | Emergency
Roll, Pitch > +/-15 degrees | Wind; misfiring thrusters; altimeter misreading | Tips over | Emergency
Rabbit Dies | Electrical misfires; batteries die | Controls inputs; engine may still fire | Emergency
Engine Fails | Air in fuel; electrical misfire; pump malfunction; dust | Coughs; fire damage; stalls completely | Flight Abort or Emergency
Altitude Control System | Batteries die; wires disconnect | Stabilizing thrusters won't work properly | Flight Abort
Z-controller Fails | Altimeter misreading; disconnection | Begins rotating irrationally | Flight Abort
Ground Comp Malfunctions/Dies | Battery; Bluetooth malfunction | Craft is running on auto | No sequence
Power Fails Non-uniformly | Batteries die; wires disconnect | See Rabbit, Engine, Controller dies | Flight Abort or Emergency
Power Fails Uniformly | Batteries die; wires disconnect | Machine drops to ground as engine stops | Flight Abort or Emergency
Notes: <number>

## Slide 60
Abort and Mission Variables would be programmed into onboard Avionics prior to flight
Notes: <number>

## Slide 61
Show a simple integration and build and test flow (Michael)
Notes: <number>

## Slide 62
Need to identify key risk areas and show we are mitigating them (Daniel/Nikita/Dave et al)
Notes: <number>